Detailed Design

sco_log

Python package for log.

Revision History
Rev.	Comment	Author

# Introduction
 This is a detailed design document for Python package sco_log. Table 1.1 shows reference materials.
Table 1.1: Reference materials.
Material	Reference
Functional Design sco_log	fd_sco_log.odt
typing — Support for type hints	typing — Support for type hints — Python documentation

 In this document, the contents that overlap with the functional design are not described as much as possible.
# sco_log.py
 Table 2.1 shows imports.
Table 2.1: sco_log.py imports.
from	import	Reference
typing	Final	Built-in.
logging	Formatter, StreamHandler, DEBUG, getLogger

 Table 2.2 shows constants.
Table 2.2: sco_log.py constants.
Constant	Use
LOG_NAME	Logger name.
LOG_LEVEL	Outputs a log with a level higher than `LOG_LEVEL`.
LOG_FORMAT	Log output format.

## LOG_NAME
LOG_NAME: Final[str] = "sco_log"
## LOG_LEVEL
LOG_LEVEL: Final[int] = DEBUG

## LOG_FORMAT
LOG_FORMAT: Final[str] = \
    "%(asctime)s - %(levelname)8s - %(pathname)s(%(lineno)4d) - " \
    "%(funcName)s()\n" \
    "%(message)s"
## sco_log_get
 Figure 2.1 shows activity diagram.
Figure 2.1: `sco_log_get` activity diagram.
## sco_log_init
 Figure 2.2 shows activity diagram.
Figure 2.2: `sco_log_init` activity diagram.